## Slide 1: Smart garbage monitoring system
Component Testing
Submitted by
Parth Patel (C0754250)

## Slide 2: LPC1768
The mbed NXP LPC1768 is one of a range of mbed Microcontrollers packaged as a small 40-pin DIP, 0.1-inch pitch form-factor making it convenient for prototyping with solderless breadboard, stripboard, and through-hole PCBs. It includes a built-in USB programming interface that is as simple as using a USB Flash Drive. Plug it in, drop on an ARM program binary, and its up and running.
NXP LPC1768 MCU
  High performance ARM Cortex™-M3 Core
  96MHz, 32KB RAM, 512KB FLASH
  Ethernet, USB Host/Device, 2xSPI, 2xI2C, 3xUART,
  CAN, 6xPWM, 6xADC, GPIO
Prototyping form-factor
  40-pin 0.1" pitch DIP package, 54x26mm
  5V USB or 4.5-9V supply
  Built-in USB drag 'n' drop FLASH programmer
mbed.org Developer Website
  Lightweight Online Compiler
  High level C/C++ SDK
  Cookbook of published libraries and projects

## Slide 3: Getting started with LPC1768
Connect mbed LPC1768 to a PC – After connecting LPC1768 to PC by USB cable we can see power light on the board and after few seconds, PC will recognize the mbed Microcontroller as a standard USB drive.
Click the MBED.HTM link to get logged in : Once USB drive is appeared, go to the new USB drive and click MBED.HTM to open it in a web browser. We need to create a mbed account to get access to the websites, tools, libraries and documentation.

## Slide 4: Downloading program
We can take advantage of pre-complied program to get used to downloading and running programs to check the functionality of the LPC1768.
Save and compile
Compiler output
- Error and warnings, or
- A Downloadable binary

## Slide 5: LPC1768 blinky testing
Save the binary file to USB drive
Once the file has saved to the MBED drive , it needs to be programmed into the microcontroller
Press the button on the LPC module
Code will start running.

## Slide 6: LCD 1602 testing using Arduino
LCDs are ideal for displaying text/characters only. The display has an LED backlight and can display 32 ASCII characters in two rows with 16 characters on each row.
To adjust contrast and brightness we connect 10k potentiometer between 5V and GND of Arduino and center pin of the potentiometer to pin 3 on the LCD.
LCD | Arduino | LCD | Arduino
RS | 12 | D4 | 5
ENABLE | 11 | D5 | 4
RS | GND | D6 | 3
R/W | GND | D7 | 2
VSS | GND | LED+ | 5V – 220 Ohm
VCC | 5V | LED - | GND

## Slide 7: Testing code and result

## Slide 8: Ultrasonic Sensor (HR-SC04) testing using Arduino
Ultrasonic sensor emits an ultrasound at 40 000 Hz which travels through the air and if there is an object or obstacle on its path, it will bounce back to the module. Considering the travel time and the speed of the sound you can calculate the distance.
The HC-SR04 Ultrasonic Module has 4 pins, Ground, VCC, Trig and Echo. The Ground and the VCC pins of the module needs to be connected to the Ground and the 5 volts pins on the Arduino Board respectively and the trig and echo pins to Digital I/O pin on the Arduino Board.

## Slide 9: Testing code :
We can set the distance as per our requirement between (2cm- 400cm)
As sensor detects any object in specified range, an LED on Arduino board is start blinking otherwise, an LED remains off.

## Slide 10: Results :

## Slide 11: ESP8266 Wi-Fi module testing using Arduino with ThingSpeak
ESP8266 Wi-Fi module is low cost standalone wireless transceiver that can be used for end-point IoT developments.
ESP8266 Wi-Fi module enables internet connectivity to embedded applications. It uses TCP/UDP communication protocol to connect with server/client.
To communicate with the ESP8266 wifi module, microcontroller needs to use set of AT commands. Microcontroller communicates with ESP8266-01 Wi-Fi module using UART having specified Baud rate.

## Slide 12: Schematic connection:
ESP8266 | Arduino
RX | RX
TX | TX
GND | GND
VCC | 3.3 V
EN | 3.3 V
GPIO 0 | NONE
GPIO 2 | NONE

## Slide 13: Setting up ThingSpeak :
Thingspeak is an open IOT platform where anyone can visualize and analyze live data from their sensor devices. Also, we can perform data analysis on data posted by remote devices.
Create an account on ThingSpeak
Create a new channel with one field label
Get the API key

## Slide 14: Testing code

## Slide 15: Results

## Slide 16: References :
Administrator, Says, Z., Zhong, Says, K., Karl, Says, P., . . . Zach. (2018, April 17). Connect ESP8266 to ThingSpeak: Using AT Commands & Arduino. Retrieved October 19, 2020, from https://www.electronicshub.org/connect-esp8266-to-thingspeak/
Team, T. (n.d.). "Hello World!" Retrieved October 19, 2020, from https://www.arduino.cc/en/Tutorial/LibraryExamples/HelloWorld
Mbed NXP LPC1768 Getting Started - Handbook. (n.d.). Retrieved October 19, 2020, from https://os.mbed.com/handbook/mbed-NXP-LPC1768-Getting-Started
Mbed NXP LPC1768 Getting Started - Handbook. (n.d.). Retrieved October 19, 2020, from https://os.mbed.com/handbook/mbed-NXP-LPC1768-Getting-Started
AnirudhT1, & Instructables. (2017, September 30). Ultrasonic Sensor Testing With Arduino. Retrieved October 19, 2020, from https://www.instructables.com/Ultrasonic-Sensor-Testing-With-Arduino/